## Slide 1: .crash course
Christina Protopapadaki, Filip Jorissen & Bram van der Heijde
Christina.Protopapadaki@bwk.kuleuven.be Filip.Jorissen@mech.kuleuven.be,
Bram.vanderHeijde@kuleuven.be
October 20, 2017

## Slide 2: Modelica crash course
What is Modelica ?
Syntax, language concepts and model structuring
Modelica tools
Use of IDEAS library
Getting started (tutorials, reference docs, libraries, software implementations, ...)
 To get you started with Modelica!

## Slide 3: What is Modelica?

## Slide 4: What is Modelica
Modelica is a language for modeling of physical systems
  open source
  object oriented
  Acausal modeling (equation based)
  multi-domain
  primarily for simulation, but usable for optimization
  small and large models (> 100 000 equations)
  many model libraries (free and commercial)
  textual and graphical modeling

## Slide 5
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 6: What is Modelica?
Modeling and simulation of complex physical systems
But optimization is possible
  JModelica

## Slide 7: What is Modelica?
Language, not a tool
Tools:
  Dymola
  OpenModelica
  JModelica
Different tools
 Different functions
 Possibly slightly different results
Check www.modelica.org for more information

## Slide 8: Multi-physics environment

## Slide 9: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
Notes: Slide Michael wetter

## Slide 10: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
What if we want to change heat injection to here?
Notes: Slide Michael wetter

## Slide 11: Modelica vs. Simulink-style
Slide from Michael Wetter and Thierry Nouidui, Introduction to Modelica (2015), see http://simulationresearch.lbl.gov/modelica/downloads/workshops/2015-06-22-lbnl/slides/modelica-intro.pdf
Notes: Slide Michael wetter

## Slide 12: How does Dymola work?

## Slide 13: Modelica environments
Commercial software tool
Dymola (Dassault Systèmes, Sweden)
Free and open source tools
OpenModelica (Open Source Modelica Consortium, Sweden and other countries)
JModelica (Modelon, Sweden)

## Slide 14: What does Dymola do?
First translates, then compiles and integrates equations
  Finds solution to ODEs at indicated times
  
  Different solvers
    Radau, Dassl, Euler, Runge-Kutta,…
    Define start and end time, time step
    Define Solver tolerance or fixed time step
Simulates model
Plots output

## Slide 15: Graphical user interface
Icon view

## Slide 16: Graphical user interface
Diagram view

## Slide 17: Graphical user interface
Documentation view

## Slide 18: Graphical user interface
Modelica Text view
Notes: icon toevoegen

## Slide 19: Graphical user interface
Simulation tab

## Slide 20: Use of Dymola with KULeuven license
Access to a floating licence (on the building physics server).
Connect to WiFi
Open Dymola and go to Help > License…
Enter 10.112.72.4 and follow instructions

## Slide 21: Modelica syntax and concepts

## Slide 22: Your first model
Notes: Define variable, define equation, define initial state

## Slide 23: Your second model
Notes: Possible to define parameters: variables of which the value is known before, but can be changed by the user
Constants are used for parameters that are not likely to change

## Slide 24: Assigning units

## Slide 25: Physical types
Define own types
Use predefined SI units
  e.g. Modelica.SIunits.Voltage

## Slide 26: Documentation
Provide info to make code readable!
Notes: types: assign unit to for example real, Boolean,…

## Slide 27: Equations
Arithmetic operators
  * / + - ^ (use . for element-wise)
Time derivatives
  der(x) = x ~
  PDEs only after discretization or using specialized functions
Acausality
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a programming language. Overview of the most important parts of the syntax

## Slide 28: Logical operators, control flow
Logical
  and or not … (see modelica specification for more)
Conditional
  if elseif else
Loops
  for
Comparing numbers
  > < <> >= …
Check syntax!

## Slide 29: Let’s connect
Make two or more models interact
  Electrical circuit
  Building
  Car
  …
Need connectors
Source DOI: 10.4271/2007-01-0541, Simic et al.

## Slide 30: Connectors
Usually
  Signal in out
  Fluid flow (mass flow rate, pressure, enthalpy)
  Heat flow (heat flow rate, temperature)
Refer to one or more types
  Allow only connections between equal connectors
Notes: Types uitleggen => enkel juiste connecties maken

## Slide 31: Connectors
Three examples:
Variables with and without “flow”
  Flow variables
  Potential variables
  Stream variables
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Heat transfer
Temperature
Heat flow
Fluid flow
Pressure
Mass flow
Specific enthalpy flow
Electricity
Voltage
Current
Notes: eerst flow uitleggen

## Slide 32: Inheritance
Model inherits from other model
  Variables, parameters, equations
partial model ( extends)
Code can be managed more easily
Example

## Slide 33: Inheritance
Partial
TwoPort
Resistance
extends TwoPort
Capacitance
extends TwoPort
Inductance
extends TwoPort
Notes: Ander voorbeeld zoeken?

## Slide 34: Homework exercise

## Slide 35: Websites
General
www.modelica.org
www.openmodelica.org
www.jmodelica.org
http://www.claytex.com/tech-blog/
Modelica language
http://modref.xogeny.com/
http://book.xogeny.com/ !!!
Libraries:
https://github.com/open-ideas --> IDEAS + Crash Course
https://simulationresearch.lbl.gov/modelica --> look at Buildings.Examples.Tutorial
IBPSA Project 1: https://github.com/ibpsa/modelica-ibpsa
Dymola user guide
Volume 1 & 2: C:\Program Files (x86)\Dymola 2017\Documentation\Dymola User Manual Volume 1 or via Dymola > help.

## Slide 36: Forums
http://www.openmodelica.org/index.php/forum
http://www.jmodelica.org/forum
www.stackoverflow.com (tag Modelica)

## Slide 37: Interface with other programs
Scripting
  Parameter variation
  Parallel simulations
  Optimal control
Python scripts
  Nice for plotting
  BuildingsPy (http://simulationresearch.lbl.gov/modelica/buildingspy/)
  Built-in interface
MATLAB
  Built-in with Dymola

## Slide 38: Components
Instances of a model
model name usually Capitalized, instance not
  Wall innerWall(res = 200, A = 10);
public variables and parameters can be accessed with dot notation, e.g.:
  heatPort.Qflow
  wall.res
Protected variables/params cannot be accessed
  Don’t show up in simulation results
Notes: Naar deel libraries?  Filip